## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 2: Introduction – Part 2

## Slide 2: Today’s agenda
Challenges of communicating over a shared network – continued
Network performance measures
A high-level overview of the Internet
  The “nuts-and-bolts” view of the Internet
    Internet structure
    Network edge: access networks
    Network core
  The service view of the Internet

## Slide 3: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 4: Recap: Communicating over a shared network
To make that happen, networking people have to solve several challenging problems:
  How to decide when a sender gets to transmit data?
  How to pick good paths for getting data from its source to its destination?
  How to adapt when a switch/router or a link fails?
  …
This is where we ended last time

## Slide 5: Communicating over a shared network
To make that happen, networking people have to solve several challenging problems:
  How to decide when a sender gets to transmit data?
  How to pick good paths for getting data from its source to its destination?
  How to adapt when a switch/router or a link fails?
  …

## Slide 6
A
Information about the packet’s destination is included in the arriving packet.
Towards host A
Many different potential paths to the destination.
Routing: Picking the “best route”
Introduction: 1-6
Which one would you pick? Why?

## Slide 7: Routing: Picking the “best route”
Towards host A
A
Information about the packet’s destination is included in the arriving packet
Suppose we want the network to pick the middle path.
Introduction: 1-7
Each device is an independent entity, though
How do they coordinate to make sure to pick the middle path for packets going to A?

## Slide 8: Routing: Picking the “best route”
Towards host A
A
Information about the packet’s destination is included in the arriving packet
Suppose we want the network to pick the middle path.
Each device is an independent entity, though
How do they coordinate to make sure to pick the middle path for packets going to A?
  Routing protocols!
Introduction: 1-8

## Slide 9: (Distributed) Routing Protocols
A
Information about the packet’s destination is included in the arriving packet
Towards host A
R1
R2
R5
R4
R3
R6
Through routing protocols, network devices
  exchange messages about their routes to different destinations.
  coordinate on a (good) end-to-end path.
Introduction: 1-9

## Slide 10: (Distributed) Routing Protocols
A
Information about the packet’s destination is included in the arriving packet
Towards host A
R1
R2
R5
R4
R3
R6
I can reach A!
Through routing protocols, network devices
  exchange messages about their routes to different destinations.
  coordinate on a (good) end-to-end path.
Introduction: 1-10

## Slide 11: (Distributed) Routing Protocols
A
Information about the packet’s destination is included in the arriving packet
Towards host A
R1
R2
R5
R4
R3
R6
I can reach A through R3!
I can reach A through R3!
I can reach A through R3!
Through routing protocols, network devices
  exchange messages about their routes to different destinations
  coordinate on a (good) end-to-end path.
Introduction: 1-11

## Slide 12: (Distributed) Routing Protocols
A
Information about the packet’s destination is included in the arriving packet
Towards host A
R1
R2
R5
R4
R3
R6
I can reach A through R3!
I can reach A through R3!
I can reach A through R3!
Through routing protocols, network devices
  exchange messages about their routes to different destinations.
  coordinate on a (good) end-to-end path.
Based on the configured metrics, the path through R4 is the best!
Introduction: 1-12

## Slide 13: Routing protocols are difficult to design
A
Information about the packet’s destination is included in the arriving packet
Towards host A
R1
R2
R5
R4
R3
R6
There are many factors to consider
  Message overhead
  Convergence time
  Metrics to decide the “best” route
  …
We’ll learn about these later in the course!
I can reach A through R3!
I can reach A through R3!
I can reach A through R3!
Based on the configured metrics, the path through R4 is the best!
Introduction: 1-13

## Slide 14: Communicating over a shared network
To make that happen, networking people have to solve several challenging problems:
  How to decide when a sender gets to transmit data?
  How to pick good paths for getting data from its source to its destination?
  How to adapt when a switch/router or a link fails?
  …

## Slide 15: Communicating over a shared network
To make that happen, networking people have to solve several challenging problems:
  How to decide when a sender gets to transmit data?
  How to pick good paths for getting data from its source to its destination?
  How to adapt when a switch/router or a link fails?
  …
We will discuss these challenges, along with other challenging problems and some of the well-known solutions in the course

## Slide 16: What is a “good” network?
So far, we have discussed
  What a computer network is
  The fact that a computer network is typically shared among many traffic flows
  Some of the challenges in designing a shared network infrastructure
Now, suppose we have come up with some solutions to the above challenges and have designed a computer network.
How do we know it is a “good” network?
  High performance? How do we measure performance?
  Highly secure?
  …?
Introduction: 1-16

## Slide 17: What is a “good” network?
Introduction: 1-17
So far, we have discussed
  What a computer network is
  The fact that a computer network is typically shared among many traffic flows
  Some of the challenges in designing a shared network infrastructure
Now, suppose we have come up with some solutions to the above challenges and have designed a computer network.
How do we know it is a “good” network?
  High performance? How do we measure performance?
  Highly secure?
  …?

## Slide 18: Network performance metrics
End-to-End Delay
how long does it take for a piece of data to go from one end of the network to the other?
Loss
how often does the network lose data during transfer?
Throughput
How much data per second can the network transfer?
Introduction: 1-18
Notes: TODO: add graphics for each one!

## Slide 19: Network performance metrics
End-to-End Delay
how long does it take for a piece of data to go from one end of the network to the other?
Loss
how often does the network lose data during transfer?
Throughput
How much data per second can the network transfer?
Introduction: 1-19
Notes: TODO: add graphics for each one!

## Slide 20: End-to-End delay
End-to-end delay: how long does it take for a piece of data to go from one end of the network to the other, e.g., from A to C?
A
B
C
R1
R2
Introduction: 1-20

## Slide 21: Network Delay
D(x, y): time it takes for packet to go from x to y.
D(x): time it takes for the packet to go through x
D(A, C) =
A
B
C
R1
R2
Introduction: 1-21
D(A, R1)
+ D(R1)
+ D(R1, R2)
+ D(R2)
+ D(R2, C)

## Slide 22: Network delay over a link
: The time it takes for all the L bits in the packet to go from A onto the link (it depends on the packet ’s length)
: The time it takes for one bit to transfer from A to R1
Link rate: R bps
Link propagation delay (in sec.)
L bits in
the packet
A
R1
P
Introduction: 1-22

## Slide 23: Network delay over a link
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans (A, R1, P) = L/R
dprop: propagation delay:
m: length of physical link
s: propagation speed (~2x108 m/sec)
dprop (A, R1) = m/s
Link rate: R bps
Link propagation delay: m/s sec.
L bits in
the packet
A
R1
P
Introduction: 1-23

## Slide 24: Network delay over a link
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans (A, R1, P) = L/R
dprop: propagation delay:
m: length of physical link
s: propagation speed (~2x108 m/sec)
dprop (A, R1) = m/s
dtrans and dprop
very different
Link rate: R bps
Link propagation delay: m/s sec.
L bits in
the packet
A
R1
P
Introduction: 1-24

## Slide 25: Caravan analogy #1
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service a car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka link)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth
Introduction: 1-25

## Slide 26: Caravan analogy #2
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
Introduction: 1-26

## Slide 27: Network delay within a node
Processing
delay
A
B
dproc: processing delay
Time it takes to process the packet 
  check bit errors
    What are some possible causes of bit errors?
  determine output link
  …
typically < microsecs
Introduction: 1-27

## Slide 28: Network delay within a node
packets queue up in network device buffers, waiting for turn for transmission
Processing
delay
A
B
Queueing delay
Introduction: 1-28

## Slide 29: Network delay within a node
packets queue up in network device buffers, waiting for turn for transmission
  Queue length grows when arrival rate to link (temporarily) exceeds output link capacity
  When could this happen?
Processing
delay
A
B
Queueing delay
Introduction: 1-29

## Slide 30: Example of queue build-up in a network device
Processing
delay
A
B
Queueing delay
Suppose each link can transfer 4 packets per second in each direction
Suppose A and B each send 4 packets on L1 and L2, respectively, in one second, and all 8 packets are supposed to go out L3.
L3 can only send 4 packets out in one second
The next 4 should wait in the queue another second before they are transmitted.
L1
L2
L3
Introduction: 1-30

## Slide 31: Network delay within a node
Processing
delay
A
B
Queueing delay
dqueue: queueing delay
time waiting at output link for transmission
depends on how ”congested” that link is.
Introduction: 1-31

## Slide 32: Network delay within a node
Processing
delay
A
B
Queueing delay
dqueue: queueing delay
time waiting at output link for transmission
depends on how ”congested” that link is.
Traffic intensify . is the average packet arrival rate.
Introduction: 1-32
See page 40 in the book for a more ”formal” intuition.
Notes: Add this figure to show the significance of the queueing delay

## Slide 33: Queueing delay (revisited)
R=link bandwidth (bps)
a=average packet arrival rate
L=packet length (bits)
La is average bits arrival rate
traffic intensity = La/R
La/R ~ 0: ?
  average queueing delay small
La/R -> 1:
  delays become large
La/R > 1:
  more “work” arriving than can be serviced, average delay infinite!
Introduction: 1-33

## Slide 34: Putting all the delay components together
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs
Introduction: 1-34

## Slide 35: Putting all the delay components together
Processing
delay (dproc)
A
B
Queueing delay (dqueue)
Transmission delay (dtrans)
Propagation
delay (dprop)
The end-to-end delay for a packet:
the sum of dproc , dqueue, dtrans , and dprop for all the components (devices and links) along the path.
Introduction: 1-35

## Slide 36: Putting all the delay components together
D(x, y): transmission delay + propagation delay
D(x): processing delay + queueing delay
D(A, C) = D(A, R1) + D(R1) + D(R1, R2) + D(R2) + D(R2, C)
A
B
C
R1
R2
Introduction: 1-36

## Slide 37: Network performance metrics
End-to-End Delay
how long does it take for a piece of data to go from one end of the network to the other?
Loss
how often does the network lose data during transfer?
Throughput
How much data per second can the network transfer?
Introduction: 1-37
Notes: TODO: add graphics for each one!

## Slide 38: Packet loss
Packet loss/drop happens when a packet’s transmission over the network is aborted before it reaches the destination.
Two common causes for packet loss are
corruption and network congestion
Loss due to corruption: if, for any reason, packet bits are corrupted during transfer, network devices may be able to detect that and drop that packet.
Introduction: 1-38

## Slide 39: Packet loss due to congestion
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
A
B
packet being transmitted
buffer
(waiting area)
packet arriving to
full buffer is lost
queues (aka buffers) in network devices have finite capacity
packet loss occurs when memory to hold queued packets fills up
That is, packets arriving to full queue are dropped (aka lost)
lost packet may be retransmitted by?
  previous node
  source end system
  not at all
Introduction: 1-39

## Slide 40: Network performance metrics
End-to-End Delay
how long does it take for a piece of data to go from one end of the network to the other?
Loss
how often does the network lose data during transfer?
Throughput
How much data per second can the network transfer?
Introduction: 1-40
Notes: TODO: add graphics for each one!

## Slide 41: Throughput
Throughput ➝rate (bits/time unit)
Suppose we abstract a segment of a network as a data pipe.
To find the throughput of that segment, we measure how many bits exit the end of the pipe within one time unit.
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
into pipe
admits/accepts data at rate (Rs bits/sec)
admits/accepts data
at rate (Rc bits/sec)
Introduction: 1-41

## Slide 42: Throughput vs Delay
Suppose the “pipe”’s throughput is R bits/sec and its propagation delay is sec.
If we look at the end of the pipe, R bits of data exit (or enter) the pipe in one second.
It takes each bit sec. to go from one end of the pipe to the other.
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
into pipe
admits/accepts data at rate (Rs bits/sec)
admits/accepts data
at rate (Rc bits/sec)
Introduction: 1-42
Notes: Change delay notation from L to d

## Slide 43: Throughput
Rs < Rc What is end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
Introduction: 1-43

## Slide 44: Throughput: network scenario
Suppose 10 connections (fairly) share backbone link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput:?
min(Rc,Rs,R/10)
in practice: Rc or Rs is often smaller than R/N
  Bottleneck link is often closer to the edge of the network.
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/
…
…
Introduction: 1-44

## Slide 45: Throughput units: bps
bps = bits per second
  1 byte = 8 bits or 1 B = 8 b
In networking, K/M/G are powers of
  K or Kilo:
  M or Mega:
  G or Giga:
  …
Q: MBps = ? Bps = ? bps

## Slide 46: Network performance metrics
End-to-End Delay
how long does it take for a piece of data to go from one end of the network to the other?
Loss
how often does the network lose data during transfer?
Throughput
How much data per second can the network transfer?
Introduction: 1-46
Notes: TODO: add graphics for each one!

## Slide 47: What you need to know about network performance metrics
Given a scenario, you should be able to compute different kinds of delay, loss, and throughput.
You should know the difference between throughput and delay
There will be some questions in this week’s quiz for practice, and we will solve some of them in class next week.
Introduction: 1-47

## Slide 48: Recap: networks are complex!
They have many pieces
  Hosts, routers/switches (network devices), links, protocols, …
They can get quite large
  Thousands if not millions of hosts and devices
They are often shared among many traffic flows
Making it challenging to design efficient and effective networks
There are various metrics to measure their performance
…
Introduction: 1-48

## Slide 49
Introduction
What is a computer network? ✔︎
What is the Internet?
Introduction: 1-49

## Slide 50
Introduction
What is a computer network? ✔︎
What is the Internet?
Introduction: 1-50

## Slide 51: Internet – connecting billions of users
Data source: OWID based on International Telecommunication Union (via World Bank) and UN (2022)
PC
server
laptop
cellphone
Internet of Things
Internet
refrigerator
Autonomous vehicles
Tweet-a-watt:
monitor energy use

## Slide 52: The Internet: a “nuts-and-bolts” view
Internet
Billions of connected computing devices
running applications
PC
server
laptop
cellphone
routers/switches
ISP: internet service provider
Switches/routers that forward packets (chunks of data)
Communication links:
  fiber, copper, radio, satellite
wired links
access points

## Slide 53: The Internet: A network of networks
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Switches/routers that forward packets (chunks of data)
Communication links:
  fiber, copper, radio, satellite
Billions of connected computing devices
running applications
PC
server
laptop
cellphone
wired links
access points
routers/switches
ISP: internet service provider

## Slide 54: A packet passes through many networks
Sender
Receiver
Access network
Access network
Local/reginal network
Local/reginal network
National/global network
Network edge
Network Core
Network edge
Notes: Digitalize?

## Slide 55: A packet passes through many networks
Sender
Receiver
Network edge
Access network
Access network
Local/reginal network
Local/reginal network
National/global network
Network Core
Network edge
Notes: Digitalize?

## Slide 56: A packet passes through many networks
Sender
Receiver
Network edge
Access network
Access network
Local/reginal network
Local/reginal network
National/global network
Network Core
Network edge
Notes: Digitalize?

## Slide 57
End systems = hosts
connected computing devices
running applications that communicate with applications on other end systems
The network edge
Local/reginal ISP
Hosts
Network edge

## Slide 58
End systems = hosts
connected computing devices
running applications that communicate with applications on other end systems
The network edge
Access network
Local/reginal ISP
Access networks
access networks connect end systems to the edge routers
edge router = entry point to the Internet
wired or wireless
Hosts
Network edge

## Slide 59: Network edge - access networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
There are different kinds of access networks:
residential access networks
wireless access networks (WiFi, 4G/5G)
enterprise (Institutional) access networks
  school, company, etc.
data center networks
…

## Slide 60: Wireless access networks
Shared wireless access network connects end system to router
via base station aka “access point”
Wireless local area networks (WLANs)
  typically within or around building (~30 m)
to Internet
to Internet
Wide-area cellular access networks
  provided by mobile, cellular network operator (10’s km)
  4G/5G cellular networks

## Slide 61: Data center networks
high-bandwidth links (10s to 100s Gbps) connect hundreds to thousands of servers together, and to Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Courtesy: Massachusetts Green High Performance Computing Center (mghpcc.org)

## Slide 62: Enterprise access networks
companies, universities, etc.
  mix of wired, wireless link technologies, connecting a mix of switches and routers.
Ethernet
switch
institutional mail,
web servers
institutional router
Enterprise link to
ISP (Internet)

## Slide 63: A packet passes through many networks
Sender
Receiver
Network edge
Access network
Access network
Local/reginal network
Local/reginal network
National/global network
Network Core
Network edge
Notes: Digitalize?

## Slide 64: A packet passes through many networks
Sender
Receiver
Network edge
Access network
Access network
Local/reginal network
Local/reginal network
National/global network
Network Core
Network edge
Notes: Digitalize?

## Slide 65: Network core ➝ Connecting access networks
hosts connect to Internet via access networks
access networks in turn must be interconnected
    so that any two hosts (anywhere!) can send packets to each other
resulting network of networks (i.e., network core) is very complex
    evolution driven by economics, national policies
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Introduction: 1-65

## Slide 66: Network core ➝ Connecting access networks
Question: given millions of access networks, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Introduction: 1-66

## Slide 67: Network core ➝ Connecting access networks
…
…
…
…
…
Question: given millions of access networks, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access networks to each other directly doesn’t scale: O(N2) connections.
Introduction: 1-67

## Slide 68: Network core ➝ Connecting access networks
…
…
…
…
…
Question: given millions of access networks, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access networks to each other directly doesn’t scale: O(N2) connections.
Sounds familiar?
Introduction: 1-68

## Slide 69: Network core ➝ Connecting access networks
Option: connect each access network to one global transit ISP?
Customer and provider have economic agreement.
global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Introduction: 1-69

## Slide 70: Network core ➝ Connecting access networks
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
Introduction: 1-70

## Slide 71: Network core ➝ Connecting access networks
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. who will want to be connected
IXP
peering link
Internet exchange point
IXP
Introduction: 1-71

## Slide 72: Network core ➝ Connecting access networks
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
IXP
IXP
access
net
access
net
regional ISP
access
net
access
net
access
net
Introduction: 1-72

## Slide 73: Network core ➝ Connecting access networks
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services and content close to end users
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP
Introduction: 1-73

## Slide 74: Content provider network
Google : one of the leading examples of content-provider network.
19 major data centers distributed across North America, Europe, Asia, South America, and Australia
Each data center having tens or hundreds of thousands of servers
All are interconnected via Google’s private TCP/IP network, which spans the entire globe, separate from the public Internet
Google private network only carries traffic to/from Google servers

## Slide 75: Network core ➝ Connecting access networks
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Regional ISP
Regional ISP
Tier 1 ISP
Tier 1 ISP
IXP
Google
IXP
IXP
Introduction: 1-75

## Slide 76: The Internet: a “nuts-and-bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4/5G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force
  IEEE 802.11 for WiFi
Introduction: 1-76
Notes: IEEE 802.11 for WiFi

## Slide 77: The Internet: a “nuts-and-bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Switches/routers that forward packets (chunks of data)
Communication links:
  fiber, copper, radio, satellite
Billions of connected computing devices
running applications
PC
server
laptop
cellphone
wired links
access points
routers/switches
ISP: internet service provider

## Slide 78: The Internet: a “services” view
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to and use Internet transport service
  provides service options, analogous to postal service
Introduction: 1-78

## Slide 79
Introduction
What is a computer network? ✔︎
What is the Internet? ︎✔︎

## Slide 80: Questions?