## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 12: Network Layer – Part 4

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding

## Slide 4: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding

## Slide 5: Challenges in the Internet routing
ISP 3
ISP 1
ISP 2
subnet 3A
subnet 3B
subnet 2A
subnet 2B
Our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
Notes: Digitalize?

## Slide 6: Challenges in the Internet routing
ISP 3
ISP 1
ISP 2
subnet 3A
subnet 3B
subnet 2A
subnet 2B
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network
Notes: Digitalize?

## Slide 7: Challenges in the Internet routing
ISP 3
ISP 1
ISP 2
subnet 3A
subnet 3B
subnet 2A
subnet 2B
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network
Solution: Hierarchical Routing
Notes: Digitalize?

## Slide 8: Hierarchical routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among routers within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 9: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 10: Intra-AS routing’s role in an AS’s data forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined inside of AS1:
AS1 intra-domain routing must:
learn which destinations reachable within AS1
What are the best routes, within AS1, to get to those destinations
  i.e., the destination subnet is attached to one of AS1’s routers

## Slide 11: Inter-AS routing’s role in an AS’s data forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1 (e.g., 1c, or 1b), but which one?

## Slide 12: Advantages of hierarchical routing
Scaling to large networks
  it works for millions of routers
Incorporating policy decisions
  operators of different domains make their own routing decisions
  Intra-AS routing focuses on performance (least cost paths)
  Inter-AS routing focuses more on policy

## Slide 13: Internet routing protocols
  Inter-AS
  Intra-AS
  Link state
  Distance vector
  OSPF
  RIP
  EIGRP
  BGP

## Slide 14: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding

## Slide 15: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements to all other routers in entire AS
    directly over IP rather than using TCP/UDP (upper-layer protocol of 89)
    Responsible for reliable message transfer
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table

## Slide 16: OSPF (Open Shortest Path First) routing
security: all OSPF messages authenticated (to prevent malicious intrusion)
link costs are configured by network admin
  multiple link costs metrics possible: bandwidth, delay
support for hierarchy within a single AS
  Two levels: backbone, local area

## Slide 17: Other common intra-AS routing protocols
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
  no longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])

## Slide 18: Make sure you know
What an Autonomous System (AS) is
What Intra-AS routing means
What Inter-AS routing means
How the two work together to find paths from any source to any destination
  E.g., suppose you have a network with many AS. Suppose you are given a packet whose source is in one AS and its destination in another AS. How would the network of networks know how to forward this packet? What if the destination is in the same AS?
What are the features of OSPF?

## Slide 19: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding

## Slide 20: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
intra-AS (aka “intra-domain”): routing among routers within same AS (“network”)
inter-AS (aka “inter-domain”): routing among AS’es
Notes: Each router then locally runs Dijkstra’s shortest-path algorithm to determine a shortest-path tree to all subnets, with itself as the root node.
AS (ISP, part of an ISP, Uwaterloo campus network)
Intra-AS- performance based
Inter-AS- policy focused

## Slide 21: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  obtain destination network reachability info from neighboring ASes (eBGP)
  Decides which routes to use based on reachability information and policy
  propagates reachability information to all AS-internal routers (iBGP)
  advertise (to neighboring networks) destination reachability info
Notes: Since an inter-AS routing protocol involves coordination among multiple ASs, communicating ASs must run the same inter-AS routing protocol. In fact, in the Internet, all ASs run the same inter-AS routing protocol, called the Border Gateway Protocol, more commonly known as BGP

## Slide 22: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 23: eBGP and iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 24: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 25: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS

## Slide 26: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Path vector routing
As opposed to distance vector
Avoids ”count-to-infinity”-like problems (e.g., easy to detect loops in the path)

## Slide 27: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X
AS-PATH
NEXT-HOP

## Slide 28: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other neighboring ASes

## Slide 29: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X
NEXT-HOP
NEXT-HOP

## Slide 30: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A advertises path A,w to B and to C
B chooses not to advertise B,A,w to C!
  B gets no “revenue” for routing C,B,A,w, since none of C, A, w are B’s customers
  C does not learn about C,B,A,w path
C will route C,A,w (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w

## Slide 31: BGP: achieving policy via advertisements (more)
B
Network only wants to route traffic to/from its customers (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network

## Slide 32: BGP path advertisement: multiple paths
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 33: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 34: BGP: populating forwarding tables
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 35: BGP: populating forwarding tables
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 36: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost.
  If this is the top criteria on the list, 2d will choose 2a, even though more AS hops to X): don’t worry about how many other AS are left until the destination.
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263
1
1

## Slide 37: BGP Exercise - 1
AS2 is AS1’s and AS3’s customer. It does not want to carry their transit traffic.
X is connected to subnet 50.60.0.0/16.
Gateway routers use default BGP route selection criteria list.
Internal routers prioritize hot potato routing.
Link weights are shown in the figure
What are relevant entries in router 3c’s forwarding table for forwarding to 50.60.0.0/16? How about for router 2b? How about for router 1a?
AS3,X
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
20
10
40
30
100
50
20
80
40
40
5
1
4
3
1
1
1
1
1

## Slide 38: Answer
For 3c, only intra-domain routing matters (destination subnet is within the same AS).
  Shortest path to X is through 3a.
For 2b
  2c tells 2b it can reach the subnet with: AS-PATH AS3, NEXT-HOP 3a
  2a tells 2b it can reach the subnet with: AS-PATH AS1, AS3, NEXT-HOP 1c
  2b is prioritizing hot potato routing
    Path to 3a costs 80 (knows this through intra-domain routing)
    Path to 1c costs 70 (knows this through intra-domain routing)
  2b will choose the path advertised by 2a. Next hop in 2b’s forwarding table will be 2d.

## Slide 39: Answer
For 1a, 1c tells 1a it can reach the subnet with: AS-PATH AS3, NEXT-HOP 3a
That’s the only path to that subnet 1a knows.
Through intra-domain routing, 1a knows its shortest path is through 1b.

## Slide 40: BGP Exercise - 2
AS2 is AS1’s and AS3’s customer. It does not want to carry their transit traffic.
X is connected to subnet 50.60.0.0/16.
Gateway routers use default BGP route selection criteria list.
Internal routers prioritize hot potato routing.
Link weights are shown in the figure
What are relevant entries in router 3c’s forwarding table for forwarding to 50.60.0.0/16? How about for router 2b? How about for router 1a?
AS3,X
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
20
10
40
30
100
50
20
80
40
40
5
1
4
3
1
1
1
1
1

## Slide 41: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance

## Slide 42: What you need to know about BGP
How BGP routers communicate (i.e., BGP sessions)
  e.g., over TCP, iBGP vs. eBGP
What BGP advertisements look like
  Destination, path, next-hop

## Slide 43: What you need to know about BGP
The BGP pipeline
  Accepting/importing routes: How does the ”edge” router (gateway) decide which route to accept
  How the gateway router propagates its information to the other routers in the AS (iBGP)
  How internal routers decide how to pick paths to the outside destinations
  How gateway routers decide which routes to advertise to the neighboring AS(s).

## Slide 44: What you need to know about BGP
How do inter- and intra-AS routing interact to populate forwarding tables
  Specifically, given enough information, you should be able to figure out entries in the forwarding table.
What hot-potato routing means and the rationale behind it.
The differences between intra- and inter-AS routing
  And the rationale behind separating them.

## Slide 45: Routing – Wrap-up
We are done with routing!
Now you know how routers in the Internet find paths from a source to a destination
  Intra- and inter-domain routing
  Link state, distance vector, path vector
  OSPF, BGP
  …
Next:
  forwarding

## Slide 46: Assignment 3 (Nov. 7)
This assignment involves installing a VM and setting up some software.
We strongly encourage you to do the setup right away
  Even if you do not plan to start working on the coding yet.
The assignment has four parts
  You can get started on the early parts with what we have covered in lectures so far.
  We will cover the rest in the next few lectures
    SDN
    Middleboxes
    Link layer concepts: MAC addresses, ARP, etc.