## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 13: Network Layer – Part 5

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding

## Slide 4: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding

## Slide 5: Destination-based forwarding
Destination Prefix | Link Interface
10.20.30.0/24 | 0
5.4.0.0/16 | 1
… | …
How does the router use this for forwarding?
  When a packet comes in with destination address X
  Check whether X matches a prefix in the table
  If yes, send it to the corresponding interface (action)
  If not, drop the packet.

## Slide 6: Destination-based forwarding
Destination Prefix | Link Interface
10.20.30.0/24 | 0
5.4.0.0/16 | 1
10.20.0.0/16 | 2
… | …
What if a packet matches multiple entries?
Destination IP address:
10.20.30.5

## Slide 7: How do overlapping entries happen?
w
A
legend:
customer
network:
provider
network
B
C
x
y
10.20.30.0/24
10.20.0.0/16
B, 10.20.0.0./16
x, 10.20.30.0./24

## Slide 8: Destination-based forwarding
Destination Prefix | Link Interface
10.20.30.0/24 | 0
5.4.0.0/16 | 1
10.20.0.0/16 | 2
… | …
What if a packet matches multiple entries?
  Pick the one that has the longest prefix matching the packet’s destination
  In the above example, 10.20.30.5 matches
    the first 24 bits of 10.20.30.0/24
    the first 16 bits of 10.20.0.0/16
    So, the router picks the first entry, and sends the packet out of interface 0
Destination IP address:
10.20.30.5

## Slide 9: Destination-based forwarding
Destination Prefix | Link Interface
10.20.30.0/24 | 0
5.4.0.0/16 | 1
10.20.0.0/16 | 2
… | …
What if a packet matches multiple entries?
  Pick the one that has the longest prefix matching the packet’s destination
  i.e., the ”most specific” prefix
Destination IP address:
10.20.30.5

## Slide 10: Make sure you know
What the forwarding table looks like for destination-based forwarding
What longest-prefix matching means
E.g., Given a packet and a table, you should be able to determine what the outgoing interface is.

## Slide 11: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP

## Slide 12: The Internet needs error reporting and testing
forwarding
table
routing protocols
path selection
OSPF, BGP, ect.
IP protocol
addressing
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
What happens when something goes wrong during forwarding?

## Slide 13: ICMP: internet control message protocol
used by hosts and routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
ICMP messages carried in IP datagrams
  Still considered part of the network-layer, not transport
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 14: Traceroute and ICMP
traceroute program: provides delay measurement (RTT) from source to router along end-end Internet path towards destination
  implemented using TTL in the IP datagram header and ICMP message (type 11, code 0: TTL expired)
3 probes
3 probes
3 probes

## Slide 15: Traceroute and ICMP
when ICMP message arrives at source: record RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
source sends sets of UDP segments to destination
  1st set has TTL =1, 2nd set has TTL=2, etc.
datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 16: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP
Beyond destination-based routing and forwarding
  The end-to-end argument
  Middleboxes
  Software-defined network (SDNs)

## Slide 17: Network Layer in the Internet
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP
Beyond destination-based routing and forwarding
  The end-to-end argument
  Middleboxes
  Software-defined network (SDNs)

## Slide 18: Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge

## Slide 19: Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge

## Slide 20: The end-to-end argument
We have talked about how some of the more complex network functionality, e.g., reliable data transfer and congestion control, is implemented in the transport layer at the end points
  as opposed to inside the network (e.g., in the routers)
But that didn’t necessarily have to be the case
One could come up with a network design where these functionalities are implemented inside the network
  In fact, Infiniband networks have made different choices in this regard compared to the current Internet

## Slide 21: The end-to-end argument
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer

## Slide 22: The end-to-end argument
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer
?
?
?
?
?
?
?
?

## Slide 23: The end-to-end argument
“The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)
We call this line of reasoning against low-level function implementation the “end-to-end argument.”
Saltzer, Reed, Clark 1981
Notes: File corruption at the host (the other end has to check anyway)

## Slide 24: The end-to-end argument
In the Internet, the choice ended up being…
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer
👍
👎

## Slide 25: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers

## Slide 26: Side note: end-to-end argument is not set in stone
This was a design decision made by the designers of the Internet protocol stack to meet their requirements for the Internet
Other networks with different requirements can make different choices
For example, the InfiniBand protocol stack offers reliable data transfer at the network layer
  No packets will be lost!
  More limited in scale
  Can’t easily inter-operate with the Internet

## Slide 27: Make sure you know
What the end-to-end argument is
  With an example
How it affected the design of the Internet and its protocol stack

## Slide 28: Network Layer in the Internet
Beyond destination-based routing and forwarding
  The end-to-end argument
  Middleboxes
  Software-defined network (SDNs)
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP

## Slide 29: What if we need to do more in the network?
Internet (until early 2000s)
“intelligence” at the end point
Following the end-to-end argument, routers in the network would only do destination-based forwarding
  No parsing beyond network layer header
  No changing anything in the packet
    Except for, say, flags like ECN or TTL
But, it turned out, we may need more from the network after all.
Notes: The 20th century phone network had dumb network endpoints, really by definition. The end points were rotary phones that maybe only your parents and grandparents remember; they weren’t computers. They really were dumb devices, and therefore the phone network had programmable switches that were quite smart. All functionality – well, all of the intelligence - was implemented within the network. It HAD to be. The end systems could not do anything more than send digits and send audio signals.
When the Internet came along, the endpoints and the switches were both programmable computers. So where to put the complexity? RFC 1958 – the architectural principles of the Internet RFC - that says “intelligence is end to end rather than hidden in the network.” That puts the intelligence clearly at the edge, like we see here. And that’s possible because the edge devices are smart; they’re programmable. Well that’s the diagram as I remember it 20 years ago.
And in the 20 years since, as we see the rise of middleboxes and SDN, we’re now seeing intelligence (in software) layered on top of “dumb” whiteboxes within the network. So I might add a brain here today. And with datacenters and content distribution networks, we see even smarter and more sophisticated application-level infrastructure being connected at points within the network. So now there are clearly much much bigger, much more computationally intensive and complex, endpoints if you will in today’s Internet

## Slide 30: Middleboxes
“any intermediary box performing functions apart from normal, standard functions of an IP router on the data path between a source host and destination host”
Middlebox (RFC 3234)

## Slide 31: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: modifies IP addresses and ports
Firewalls, Intrusion Detection System (IDS): drop suspicious traffic
Load balancers: pick the server packets should go to
Caches: keep copies of popular data

## Slide 32: Middleboxes (or Network Functions)
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware
  Hardware providing an open API (programming interface)
Sometimes, high-speed implementation in software
  network functions virtualization (NFV): specialized packet processing in, say, a VM.

## Slide 33: The (more realistic) IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s new waist?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching
Do middleboxes break the end-to-end argument?

## Slide 34: What if we need to do more in the network?
Internet (until early 2000s)
intelligence, computing at edge
Internet (now)
Middleboxes/NFV
Software defined networks (SDNs)
programmable network devices

## Slide 35: Make sure you know
What a middleboxes is
Know some example middleboxes and what they do
How the functionality inside the network has changed since its early days

## Slide 36: Network Layer in the Internet
Beyond destination-based routing and forwarding
  The end-to-end argument
  Middleboxes
  Software-defined network (SDNs)
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP

## Slide 37: A more general packet processing model
Routers ➝ Forwarding table that maps destination IP addresses of incoming packets to the outgoing interface
Middleboxes ➝ Each has their own custom approach to packet processing that goes beyond what routers traditionally do
  Make decisions based on headers in other layers (e.g., transport)
  Modify packet header and/or content
  …
OpenFlow ➝ A proposal for generalized packet processing model devices in the network
  One of the original building blocks of software-defined networking (SDN)

## Slide 38: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 39: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 40: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 41: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 42: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 43: OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 44: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port

## Slide 45: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
In SDN, we call all of them (packet) switches
Even outside of SDN context, it is now quite common to use the name switches to refer to a generic network device.

## Slide 46: How does routing work in this generalized forwarding model?
The routing protocols we had learned about so far were distributed
  Every router runs an instance of the protocol
  They communicate to figure out the best forwarding paths based on costs
They were also designed with destination-based forwarding in mind.
Software-Defined Networking takes a different approach…

## Slide 47: Software-Defined Networking (SDN)

## Slide 48: Software-Defined Networking (SDN)
DP
CP
DP
CP
DP
CP
DP
CP
DP
CP

## Slide 49: Software-Defined Networking (SDN)
DP
CP
DP
CP
DP
CP
DP
CP
DP
CP
Instead of running distributed control-plane algorithms here …

## Slide 50: Software-Defined Networking (SDN)
DP
DP
DP
DP
DP
Logically Centralized Control-Plane
Run them here, and directly tell the router data plane how to forward traffic.

## Slide 51: Software-Defined Networking (SDN)
DP
DP
DP
DP
DP
Logically Centralized Control-Plane
Has a global view of the network
Has direct control over the routers

## Slide 52: Software-Defined Networking (SDN)
DP
DP
DP
DP
DP
Logically Centralized Control-Plane
Has a global view of the network
Has direct control over the routers
A control layer for local control tasks, e.g., communicating with the SDN controller.

## Slide 53: Software-Defined Networking (SDN)
DP
DP
DP
DP
DP
Logically Centralized Control-Plane
Has a global view of the network
Has direct control over the routers
A control layer for local control tasks, e.g., communicating with the SDN controller.
Generalized forwarding tables

## Slide 54: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 55: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 56: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  program the network with OpenFlow rules
  historical roots: active networking
  today: more generalized programming:
  P4 (see p4.org).

## Slide 57: Remarks on Software-Defined Networking (SDN)
SDN provides global visibility and direct control
Generalized forwarding model is one of the enablers
Why software-defined?
Because the "software" running on the SDN controller will "define" the behavior of the network
  As opposed to the interactions of several instances of a distributed protocol.

## Slide 58: Make sure you know
What generalized forwarding mean
  In contrast with (traditional) destination-based forwarding
What an OpenFlow flow table looks like and how it is used to process incoming packets
How a controller can setup rules in flow tables to determine how packets are processed in the network
E.g., given a set of paths for different traffic flows, you should be able to write down the entries in each switch flow table.

## Slide 59: SDN/OpenFlow Exercise
S1
S2
S3
S4
S5
H1
72.68.3.2
Switches should not drop any packets destined to H1, H2, or H3 unless specified by the network policy.
Web traffic between H1 and H3 should pass S3 (suppose the webserver is running on port 80).
H2 should not be able to send packets to H1
Traffic between H2 and H3 should not have any links in common with traffic between H1 and H3 (except for S5 – H3).
What do the OpenFlow rules on the switches look like?
H2
30.53.0.5
H3
12.15.63.3
1
2
1
2
3
1
2
1
2
3
1
2
3
4
3

## Slide 60: Network Layer in the Internet
Beyond destination-based routing and forwarding
  The end-to-end argument
  Middleboxes
  Software-defined network (SDNs)
The Internet Protocol (IP)
Internet Routing
  Hierarchical routing
  Intra-ISP routing: OSPF
  Inter-ISP routing: BGP
Internet Forwarding
  Destination-based forwarding
ICMP
We are done with the network layer!
Next Up: Link Layer and Local Area Networks (LANs)