## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 16: Link Layer – Part 3

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Shared LANs and multiple access protocols
  Random access

## Slide 4: Link layer: local connectivity
Either “shared link” or a link-layer network
Also called a Local Area Network (LAN)

## Slide 5: Multiple access links and protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switches and hosts
shared wire or medium (broadcast)
  old-school Ethernet
  802.11 wireless LAN, 4G/4G. Satellite
  …
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: WiFi
shared wire (e.g.,
cabled Ethernet)
shared radio: 4G/5G

## Slide 6: Multiple access protocols
single shared communication channel
two or more simultaneous transmissions by nodes can lead to interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
multiple access protocol

## Slide 7: An ideal multiple access protocol
given: multiple access channel (MAC) of rate R bps
what we ideally want:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 8: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 9: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Shared LANs and multiple access protocols
  Random access

## Slide 10: Random access protocols
when node has packet to send
  transmit at full channel data rate R
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 11: CSMA (carrier sense multiple access)
Probability of collision can be reduced if “Listen Before Talk”
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!

## Slide 12: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in determining collision probability
spatial layout of nodes

## Slide 13: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in determining collision probability
spatial layout of nodes

## Slide 14: CSMA (carrier sense multiple access)
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  monitor for incoming signals while transmitting
  if collision detected: stop sending and retry later
human analogy: If someone else starts talking at the same time, stop talking (the polite conversationalist).

## Slide 15: CSMA/CD:
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 16: CSMA/CD:
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
collisions detected within short time
colliding transmissions aborted, reducing channel wastage
spatial layout of nodes

## Slide 17: Ethernet CSMA/CD algorithm
Ethernet receives datagram from network layer, creates frame
If Ethernet senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If entire frame transmitted without collision - done!
If you detect collision, abort and wait a random amount of time (from a given range) and try again
  If collision again, pick a random wait time from a larger range next time.
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maxi- mum value that n can take is capped at 10.

## Slide 18: Ethernet CSMA/CD algorithm
If another transmission detected while sending: abort
After aborting, enter binary (exponential) backoff:
  after mth collision, chooses K at random from {0,1,2, …, 2m-1}.
  wait bit times, i.e., K times the amount of time need to send 512 bits
  returns to Step 2 (sense before sending)
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maxi- mum value that n can take is capped at 10.

## Slide 19: Ethernet CSMA/CD algorithm
If another transmission detected while sending: abort
After aborting, enter binary (exponential) backoff:
  after mth collision, chooses K at random from {0,1,2, …, 2m-1}.
  wait bit times, i.e., K times the amount of time need to send 512 bits
  returns to Step 2 (sense before sending)
more collisions: longer backoff interval
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maxi- mum value that n can take is capped at 10.

## Slide 20: Minimum frame size
Suppose A sends a frame at time t
B sees an idle channel right before t + d and starts transmitting a frame
A won’t see a collision until t + 2d
A
B
Propagation delay = d
Slides adapted from Jennifer Rexford, Princeton

## Slide 21: Minimum frame size
A should wait for time 2d to detect collision
  So, it will keep transmitting during this period
That’s why there are restrictions on “classical” Ethernet
  Maximum length of the wire: 2500 meters
  Minimum length of the frame: 512 bits (64 bytes)
A
B
Propagation delay = d
Slides adapted from Jennifer Rexford, Princeton

## Slide 22: Link characteristics affect protocol design
In wired LANs, any two nodes on the shared medium can detect collision easily
  measure signal strengths, and compare the transmitted and received signals
  Ethernet uses CSMA/CD
But, in wireless LANs, collision detection is difficult
  due to characteristics of wireless links
  wireless LANs (WiFi) uses CSMA/CA: CSMA with collision avoidance
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maxi- mum value that n can take is capped at 10.

## Slide 23: IEEE 802.11 (WiFi) MAC Protocol: CSMA/CA
Base stations (or Access point):
Connects end points via a wireless “link”
  Shared physical medium
Connect to the wired network
  E.g., the Internet
  Provide connection from user devices to the wired network

## Slide 24: Wireless link characteristics
  fading (attenuation)
  radio signal attenuates (loses power) as it propagates (free space “path loss”)
  noise
  received signal is a combination of attenuated original signal and background noise in the environment -> more “lossy” than wired link
  SNR: signal-to-noise ratio
  larger SNR -> lower bit error rate (BER) -- easier to extract signal from noise (a “good thing”)
Notes: Wikipedia figure

## Slide 25: Wireless link characteristics
Attenuation also causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 26: Wireless vs. Wired for multi-access channel
CSMA/CD tells whether or not there is some activity on the transmitter
In a wired setting, the transmitted can see all the activity on the channel. So, this is enough.
In a wireless setting, the transmitter does not necessary see all the activity on the channel.
  We need some extra mechanisms!

## Slide 27: WiFi CSMA/CA protocol
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2

## Slide 28: WiFi CSMA/CA protocol
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
Note the differences from CSMA/CD

## Slide 29: WiFi CSMA/CA protocol
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
Note the differences from CSMA/CD
Reliable delivery mechanisms in the link layer!

## Slide 30: WiFi CSMA/CA protocol
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
Note the differences from CSMA/CD
The protocol has optional extensions to reduce collisions even more…

## Slide 31: Wireless links affect higher-layer protocols
In wireless LAN, bit errors are much more common than in wired networks. Packets may often be corrupted or lost for reasons other than congestion
  but TCP will interpret any packet loss as congestion and reduce its send window
Solutions?
  Have the “wireless” link layer protocol do retransmissions
  Provide extra signals to TCP to convey if a loss is due to the nature of the wireless link rather than congestion
  …

## Slide 32: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Shared LANs and multiple access protocols
  Random access

## Slide 33: Cable access network: channel partitioning and random access!
cable headend
CMTS
ISP
cable modem
termination system
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
multiple downstream (broadcast) channels (frequency-partitioned): up to 1.6 Gbps/channel
  single CMTS transmits into channels
multiple upstream channels (up to 1 Gbps/channel)
  multiple access: all users contend (random access) for certain upstream channel time slots; others assigned (time-partitioned) channels

## Slide 34: What you need to know about multiple access channels
Know what a multiple access (or shared, or broadcast) channel is.
Know the details of CSMA/CD
  E.g., if you are given a scenario with transmissions and how long nodes will back-off after detecting collision, you should be able to follow the protocol to figure out when collisions happen and when a frame will finally be transmitted.
Know the characteristics of wireless links and how they affect protocols designs
  How does CSMA/CA work?
  How is TCP affected?

## Slide 35: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Shared LANs and multiple access protocols
  Random access

## Slide 36: Final Remarks on MAC address vs IP addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-adjacent interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in the ROM of the interface hardware, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD
Q: Why use a separate set of addresses in the link layer?
A: ??

## Slide 37: What use a separate address space in the link layer?
Network layer and link layer have different goals, hence different requirements
Network layer: global connectivity
  Need to aggregate addresses for interfaces close to each other to scale
  So, IP addresses change when a device moves
Link layer: local connectivity
  Much smaller scale -- It is ok to have fixed “random” address for the interface
  A fixed address makes it easier to bootstrap (we can still talk with the interface until it gets its IP address, more on this next week!)
Also, each local network can have its own way to forward traffic
  And still be able to connect to different kinds of networks…
  through IP, or any other network layer protocol that they all agree on.
Any other thoughts?

## Slide 38: Link layer: roadmap
Link layer overview
  Local Area Networks (LANs)
Switched LANs
  Ethernet and Addressing
  Address Resolution Protocol (ARP)
  Switches
Virtual LANs (VLANs)
Multiple access protocols
  Random access
We are done with the link layer!
Next Up: Naming and Addressing