## Slide 1: CS 456/656 Computer Networks
Mina Tahmasbi Arashloo and Uzma Maroof
Fall 2025
Lecture 17: Naming and Addressing

## Slide 2: A note on the slides
Adapted from the slides that accompany this book.
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 3: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
R
A
Destination MAC
Destination IP
Source IP
Source MAC
B
and are in the same LAN

## Slide 4: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
R
A
B
Source IP
Source MAC
First-hop router IP
First-hop router MAC
Destination IP
Destination MAC
and are in different LANs

## Slide 5: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.

## Slide 6: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.
This Lecture: How does A find these addresses?

## Slide 7: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.
Comes with the interface

## Slide 8: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.

## Slide 9: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.
How does A get an IP address ??

## Slide 10: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway (first-hop) router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.
How does A get an IP address ??
How does A find B’s (or R’s) IP address?

## Slide 11: Naming and Addressing: roadmap
DHCP
  Helps A find an IP address
  Helps A find the IP address of the gateway router
DNS
  Helps A find B’s IP address

## Slide 12: Naming and Addressing: roadmap
DHCP
  Helps A find an IP address
  Helps A find the IP address of the gateway router
DNS
  Helps A find B’s IP address

## Slide 13: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg
Notes: ICANN (Internet Corporation for Assigned Names and Numbers)
Allocating IP address
Managing DNS root servers

## Slide 14: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 15: DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 16: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
    Which we will learn about next
  network mask (indicating network versus host portion of address)

## Slide 17: DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-mux’ed to IP de-mux’ed, UDP de-mux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 18: DHCP: example
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, de-muxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 19: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.
How does A get an IP address ??
How does A find B’s (or R’s) IP address?

## Slide 20: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.
How does A get an IP address ?? DHCP
How does A find B’s (or R’s) IP address?

## Slide 21: What you need to know about DHCP
The purpose of the protocol
The protocol’s basic operations, i.e., the messages and information exchanged when a host wants to acquire an IP address.
  E.g., given a scenario where a host (re)joins a LAN, you should be able to fill out the basic information inside the exchanged messages.
The extra information that DHCP provide for hosts to bootstrap their network configurations.

## Slide 22: Naming and Addressing: roadmap
DHCP
  Helps A find an IP address
  Helps A find the IP address of the gateway router
DNS
  Helps A find B’s IP address

## Slide 23: DNS: Domain Name System
people: many identifiers:
  SIN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams in the network layer.
  “name”, e.g., cs.umass.edu - used by humans

## Slide 24: DNS: Domain Name System
people: many identifiers:
  SIN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams in the network layer.
  “name”, e.g., cs.umass.edu - used by humans
Human readable
Much easier to remember
IP addresses may change but this doesn’t have to change

## Slide 25: DNS: Domain Name System
people: many identifiers:
  SIN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams in the network layer.
  “name”, e.g., cs.umass.edu - used by humans
Q: how to map from a name to an IP address?

## Slide 26: DNS: Domain Name System
people: many identifiers:
  SIN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams in the network layer.
  “name”, e.g., cs.umass.edu - used by humans
Q: how to map from a name to an IP address?
Domain Name System (DNS):
Database that keeps the mapping between names and IP addresses
Implemented in a distributed manner over a hierarchy of name servers
application-layer protocol: hosts and DNS servers communicate to resolve names (address/name translation)
  DNS is core Internet function, implemented as application-layer protocol

## Slide 27: DNS: a distributed, hierarchical database
Client wants IP address for www.amazon.com:
client queries root server to find .com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
.com DNS servers
.org DNS servers
.edu DNS servers
…
…
Top Level Domain
Root DNS Servers
Root
nyu.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
Authoritative
…
…
…
…

## Slide 28: DNS: root name servers
Provides the IP address of Top-Level-Domain (TLD) servers
  Right below it in the tree
They are where one goes to get the translations started.

## Slide 29: DNS: root name servers
incredibly important Internet function
  Internet couldn’t function without it!
ICANN (Internet Corporation for Assigned Names and Numbers) manages root DNS domain
13 logical root name “servers” worldwide each “server” replicated many times (~200 servers in US)

## Slide 30: Top-Level Domain, and authoritative servers
Top-Level Domain (TLD) servers:
  responsible for names under .com, .org, .net, .edu, .aero, .jobs, .museums, and all top-level country domains, e.g.: .cn, .uk, .fr, .ca, .jp
  Network Solutions: authoritative registry for .com, .net TLD
  Educause: .edu TLD
authoritative DNS servers:
  organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 31: DNS name resolution
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
authoritative DNS server
dns.cs.umass.edu
TLD DNS server

## Slide 32: Local DNS name servers
when host makes DNS query, it is sent to its local DNS server
  Local DNS server returns reply, answering:
    from its local cache of recent name-to-address translation pairs
    forwarding request into DNS hierarchy for resolution if not in cache
  each ISP has local DNS name server; to find yours:
    MacOS: % scutil --dns
    Windows: >ipconfig /all
local DNS server doesn’t strictly belong to hierarchy

## Slide 33: DNS name resolution: iterative query
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
Iterative query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 34: DNS name resolution: recursive query
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu

## Slide 35: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  Value is hostname of authoritative name server for this domain or a name server for a domain that includes the hostname
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of SMTP mail server associated with name

## Slide 36: Example of records
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu IP address: 128.119.245.12
root DNS server
IP address: 8.5.1.4
local DNS server
dns.nyu.edu
authoritative DNS server
dns.cs.umass.edu
IP address: 17.18.19.3
TLD DNS server
IP address: 15.3.120.4

## Slide 37: Example of records
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu IP address: 128.119.245.12
root DNS server
IP address: 8.5.1.4
local DNS server
dns.nyu.edu
authoritative DNS server
dns.cs.umass.edu
IP address: 17.18.19.3
TLD DNS server
IP address: 15.3.120.4
(gaia.cs.umass.edu, 128.119.245.12, A, 30)

## Slide 38: Example of records
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu IP address: 128.119.245.12
root DNS server
IP address: 8.5.1.4
local DNS server
dns.nyu.edu
authoritative DNS server
dns.cs.umass.edu
IP address: 17.18.19.3
TLD DNS server
IP address: 15.3.120.4
(cs.umass.edu, dns.cs.umass.edu, NS, 60)
(dns.cs.umass.edu, 17.18.19.3, A, 60)

## Slide 39: Example of records
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu IP address: 128.119.245.12
root DNS server
IP address: 8.5.1.4
local DNS server
dns.nyu.edu
authoritative DNS server
dns.cs.umass.edu
IP address: 17.18.19.3
TLD DNS server
IP address: 15.3.120.4
(edu, <hostname for .edu TLD>, NS, 60)
(<hostname for .edu TLD>, 15.3.120.4, A, 60)

## Slide 40: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
message header:
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative

## Slide 41: DNS protocol messages
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
DNS query and reply messages, both have same format:
name, type fields for a query
RRs in response to query
records for authoritative servers
additional “ helpful” info that may be used

## Slide 42: Caching DNS Information
once (any) name server learns mapping, it caches mapping, and immediately returns a cached mapping in response to a query
  caching improves response time
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
cached entries may be out-of-date
  if named host changes IP address, may not be known Internet-wide until all TTLs expire!
  best-effort name-to-address translation!

## Slide 43: Getting your info into the DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts NS, A RRs into .com TLD server:
  (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server locally with IP address 212.212.212.1
  type A record for www.networkuptopia.com
  type MX record for networkutopia.com

## Slide 44: DNS security
DDoS attacks
bombard root servers with traffic
  not successful to date
  traffic filtering
  local DNS servers cache IPs of TLD servers, allowing root server bypass
bombard TLD servers
  potentially more dangerous
Spoofing attacks
intercept DNS queries, returning bogus replies
  DNS cache poisoning
  RFC 4033: DNSSEC authentication services

## Slide 45: DNS: services, structure
Q: Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services:
hostname-to-IP-address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
A: doesn‘t scale!
Comcast DNS servers alone: 600B DNS queries/day
Akamai DNS servers alone: 2.2T DNS queries/day

## Slide 46: Final thoughts about the DNS
humongous distributed database:
~ billion records, each simple
handles many trillions of queries/day:
many more reads than writes
performance matters: almost every Internet transaction interacts with DNS - msecs count!
organizationally, physically decentralized:
millions of different organizations responsible for their records
Needs to be reliable and secure

## Slide 47: What you need to know about DNS
DNS is a very important protocol so almost everything we have discussed is important to know. This includes but is not limited to
The purpose of DNS and the details of how it operates
How DNS name servers are structured
Various DNS records and what they are used for
The difference between local DNS name servers and other name servers and how they interact
Various ways for a DNS query to be resolved.
Being able to fill out details the steps in resolving DNS queries (including the order in which they happen) and DNS records at various name servers
…

## Slide 48: Naming and Addressing
If host A wants to communicate with host B
A and B each should have an interface connecting them to their LAN.
Each interface should have an IP address and a MAC address.
To send data to B, A should create a packet with the following addresses:
  source IP address:
  destination IP address:
  source MAC address:
  destination MAC address: if they are in the same LAN. Otherwise, , where R is the interface of the gateway router in A’s LAN.
Comes with the interface
Through ARP. But has to know B’s (or R’s) IP address.
How does A get an IP address ?? DHCP
How does A find B’s (or R’s) IP address?
B’s IP address: DNS, R’s IP address: DHCP

## Slide 49: Naming and Addressing: roadmap
DHCP
  Helps A find an IP address
  Helps A find the IP address of the gateway router
DNS
  Helps A find B’s IP address

## Slide 50: Bringing it all together
We have covered (almost) all the main layers of a network stack!
We have also covered important protocols that help with naming and addressing.
When you come to campus, open your laptop, connect to the network, and type “www.google.com” in the browser…
All of these protocols have to work together under the hood before you can actually see google’s landing page 
Let’s walk through a (very important) example

## Slide 51: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 52: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-muxed to IP de-muxed, UDP de-muxed to DHCP

## Slide 53: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 54: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 55: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
de-muxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 56: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 57: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 58: What you need to know
This example brings together a lot of what we have talked about in this course
Make sure you are comfortable with the individual steps that are happening, and their order.
E.g., given a similar scenario, you should be able to work out what happens under the hood from when a client arrives in a network and starts using some of the network applications we have talked about.